Fuel Consumption Profile Model

  1. Analysis of available data
We first analyze some of the data from FCOM (Flight Crew Operations Manual) to determine the assumptions we can make to simplify the model. A fully-detailed fuel consumption model is very time-consuming to develop, if possible at all. The project goal requires a more practical, yet reasonably precise model. That’s why we need to establish some useful assumptions.

    1. Gross weight - fuel flow relation
 We took some data from the FCOMs of 737-800 and 777-200LR. Here are the results.

737-800
Fuel Flow per engine (kg/hr)
Gross weight (ton)

777-200LR
Fuel Flow per engine (kg/hr)
Gross weight (ton)
It’s clear that fuel flow varies almost linearly with the gross weight, even if the range of weight data is pretty large. The data used can be found in appendix.

    1. Flight distance – fuel required relation
Linear approximation is a lot less accurate in this case. Below is the fuel-distance relation of 777-200LR, with landing weights of 150 and 240 tons. Numerical data is in the appendix.

777-200LR
Fuel required (ton)
Distance (Nm)

  1. What does not work

    1. Payload-range diagram
The payload-range diagram is easily accessible on the Internet, but hidden parameters which are not specified in the diagrams cause significant inaccuracy.
Most aircraft manufacturers publish airport planning manual on the Internet, including Airbus, Boeing, Embraer, etc. The problem is that we do not know the amount of final reserve fuel, contingency fuel or distance to alternate airport used in generating these diagrams.
We will try to build a payload-range diagram from the Boeing 737-800 FCOM data, and see why the charts alone is insufficient to build an accurate fuel consumption profile. We only focus on the segment where range is limited by fuel capacity (See image below).

(Image source)

As a comparison, below is the payload-range chart in Boeing’s airport planning manual, for 737-800. In the test, we use 20,894 kg of fuel capacity and plot the ranges with 40 to 50 tons of zero fuel weight.

Here are the results with different parameters below (x-axis: range in nm, y-axis: zfw in ton). The left one assumes no final reserve, go-around, or contingency fuel. The right one assumes 45 minutes of final reserve, one go-around, and 5% contingency fuel. The results are noticeably different. At 40 tons, the range are different by about 16%. This is not acceptable.
The code which produced these charts are in code/PayloadRangeChart.

1. Appendix
  1. Gross weight - fuel flow data
Data for 737-800
Gross weight (ton)	Fuel flow per engine (kg/hr)
360	5186.5
340	4917
320	4554
300	4240
280	3976
260	3678
240	3392
220	3131
200	2878.5
180	2616.5
160	2356

Data for 777-200LR
Gross weight (ton)	Fuel flow per engine (kg/hr)
360	5186.5
340	4917
320	4554
300	4240
280	3976
260	3678
240	3392
220	3131
200	2878.5
180	2616.5
160	2356

2.2 Fuel-distance relation
Distance (Nm)	Fuel required (150 tons)	Fuel required (240 tons)
50	1.4	2.1
100	2.2	3
150	3	3.9
200	3.5	4.8
250	4.1	5.6
300	4.7	6.3
350	5.1	7
400	5.6	7.8
450	6	8.5
500	6.4	9.2
1000	11.8	16.5
1500	16.9	24.2
2000	22.1	32.2
2500	27.4	40.1
3000	32.9	48.3
3500	38.5	56.7
4000	44.2	65.5
4500	50.1	74.2
5000	56.2	83.4
5500	62.5	92.9
6000	68.9	102.8
6500	75.4	112.9
7000	82.1	123.2
7500	89	133.8
8000	96.1	144.6
8500	103.4	155.8
9000	111	167.4
9500	118.7	179.1
10000	126.6	191.3